## Slide 1: Exadata Distictives 988
Bobby Durrett
US Foods
Notes: <number>

## Slide 2: What is Exadata?
Complete Oracle database server
  Disk storage system
  CPU, memory, network hardware
  Operating system
  Database software
  Fully installed and configured

## Slide 3
Cell Storage servers
Intel-based Linux servers
with disk drives
14 cell servers per rack
7 on top, 7 on bottom
12 disks per server

## Slide 4
3 Infiniband network switches
1 on top, 2 on bottom
8 Intel Linux database servers
4 on bottom, 4 on top

## Slide 5: What is standard about Exadata?
Off the shelf hardware
  Intel x86 processors
  Standard Sun disk drives, memory
  Infiniband network adapters and switches
Linux operating system
Oracle 11gR2 database software

## Slide 6: What is unique about Exadata?
Storage Servers have Oracle database specific features
  Smart Scan – returns only needed data
  Storage Indexes – only accesses needed disk blocks
  Hybrid Columnar Compression – fits data into fewer disk blocks

## Slide 7: Comparison of three db server types
Compare three types of database servers to demonstrate features unique to Exadata
  DB server with directly attached disk drives
  DB server attached to a Storage Area Network (SAN)
  Exadata
    With Smart Scan
    Without Smart Scan

## Slide 8: Rows, Columns, and Blocks
A SQL table is a collection of rows – one row per sale
A row is a list of columns – date, product, customer, amount,…
A table is broken up into equal sized blocks each with a number of rows = block size/row size = 8000 bytes/80 bytes = 100 rows per block
Results of queries are a subset of the columns and a subset of the rows of a table

## Slide 13: Observations about the three server types
DB server with disks looks like Exadata Cell server
  Indexes
  Compression
  memory cache
  returns small subset of full data
DB server with SAN looks like full Exadata system
  Storage server
  High speed network
  Database servers

## Slide 14: More observations about the three server types
DB server with SAN differs from full Exadata system
  Full database blocks copied over SAN network
  Results only copied over Exadata network
  Database server caches blocks from SAN
  Database server does not cache results from cell server
Exadata Smart Scan can be turned off
  Without Smart Scan Exadata works just like DB server with SAN

## Slide 15: How to Use Exadata Smart Scan
Queries with full table scans automatically do Smart Scans
Drop indexes
Make indexes invisible
Increase optimizer_index_cost_adj to discourage index use
Use FULL hints to force full scans

## Slide 16: How to avoid Smart Scan
Add indexes and verify that plan uses them
Add INDEX hint to force index use
Set CELL_OFFLOAD_PROCESSING to FALSE
  alter system set CELL_OFFLOAD_PROCESSING=FALSE;
  alter session set CELL_OFFLOAD_PROCESSING=FALSE;
  hint - OPT_PARAM('cell_offload_processing' 'false')

## Slide 17: Moving an existing application to Exadata
Try these options and see which is faster:
  Indexes visible or invisible
  optimizer_index_cost_adj normal (100) or high (> 100)
  CELL_OFFLOAD_PROCESSING=FALSE or TRUE
All of these options can be tested without changing the application

## Slide 18: Why use Exadata?
New set of performance enhancing features
All other Oracle features still available
Easy to use new features
Easy to bypass new features

## Slide 19: Things to watch out for
Flash memory (storage server cache) slow
  Normal RAM – 1000x faster than disk
  Cell server cache (Flash) – 10x faster than disk
Can’t control, no documentation for storage indexes
  What columns are they on?
  What column types can they be on?

## Slide 20: Things to watch out for – page 2
Databases tuned for Exadata are not portable
  Datafiles with HCC won’t work on non-Exadata system
  Applications that have been tuned to work well on Exadata will be slow on non-Exadata
Poor performance of TEMP space
  Like all RAC systems with many nodes moving temp space from node to node kills performance.
  Newer X2-8 may address this – 2 node RAC

## Slide 21: Things to watch out for – page 3
HCC and tables > 255 columns buggy
  Wrong results, errors
  Wrong optimizer stats
Newness issues
  Bugs, hangs, crashes, unexpected results
  Lack of documentation
  Lack of trained people

## Slide 22: Recommendations
Small number of RAC nodes – 2 if possible
Use as few new features as possible
Fewer than 256 columns per table
Get Exadata VM from Oracle for sandbox
Exalogic – can connect to DB via Infiniband
Switch our DB links to IB